WHITE SAIL III

PRACTICAL SKILLS CHECKLIST

| Date: |  | Training Hours: | Name: |  |
| --- | --- | --- | --- | --- |
| Average Wind speed : |  |  | Boat Type: |  |
| D.O.B: (D/M/Y) |  |  | Evaluation: | WS III or WS III IP |

The LTS/R committee recommends that sailors spend a minimum of 30 hours completing the skills below before moving on to the Bronze Sail IV skills.  Advancement prior to completion of the 30-hour practice time is authorized when a sailor can demonstrate all skills consistently.

| SKILLS | - Not Demonstrated (ND) - Demonstrated (D) - Demonstrated Consistently (DC) |
| --- | --- |
| ASHORE | ND | D | DC |  | ND | D | DC |
| Lateral Buoy System | Port Hand |  |  |  | Starboard Hand |  |  |  |
|  | Fairway |  |  |  | Isolated Danger |  |  |  |
| Parts of the Hull | Thwart |  |  |  | Buoyancy Tank |  |  |  |
|  | Mast Step |  |  |  | Centreboard Line |  |  |  |
| Rigging Items | Cotter Pin |  |  |  | Shroud Adjuster |  |  |  |
|  | Clevis Pin |  |  |  | Split Ring |  |  |  |
| Parts of the Sail | Luff |  |  |  | Foot |  |  |  |
|  | Clew |  |  |  | Batten Pocket |  |  |  |
|  | Leech |  |  |  | Bolt Rope |  |  |  |
|  | Tack |  |  |  | Hanks |  |  |  |
|  | Head |  |  |  | Cringle |  |  |  |
| Foils | Pintle |  |  |  | Rudder Blade |  |  |  |
|  | Gudgeon |  |  |  | Rudder Head |  |  |  |
| Types of Sailboats | Cat Rigged |  |  |  | Sloop Rigged |  |  |  |
|  | Keelboat |  |  |  | Centreboard |  |  |  |
|  | Sail Board |  |  |  | Catamaran |  |  |  |
| Comments |  |
| SKILLS | Not Demonstrated | Demonstrated | Demonstrated Consistently |
| CYA Structure | Describe the major functions of the NSO, PSO, Class Associations, Member Clubs and Sailing Schools. |  |  |  |
|  | Describe the different levels within the CYA LTS program. |  |  |  |
| Hypothermia | Explain what hypothermia is and a cause. |  |  |  |
|  | List three ways to minimize hypothermia. |  |  |  |
|  | List two rules for treatment of a mild hypothermia victim. |  |  |  |
| Hazards | List three geographic hazards. |  |  |  |
|  | List three navigation hazards. |  |  |  |
| Weather | List three sources of weather information. |  |  |  |
|  | List three warning signs of weather. |  |  |  |
| Comments |  |

| AFLOAT |
| --- |
| SKILLS | Not Demonstrated | Demonstrated | Demonstrated Consistently |
| Leave Dock/Shore | Skipper identifies the wind direction. |  |  |  |
|  | Good route planning & control. |  |  |  |
|  | Proper skipper commands. |  |  |  |
|  | Crew assist skipper. |  |  |  |
| Returning to a Dock/Shore | Good route planning & control. |  |  |  |
|  | Proper skipper commands. |  |  |  |
|  | Crew assist skipper. |  |  |  |
|  | Sails are lower prior to docking. |  |  |  |
|  | Approaches head to wind. |  |  |  |
|  | Soft contact with dock. |  |  |  |
| Mooring | Good route planning & control. |  |  |  |
|  | Proper skipper commands. |  |  |  |
|  | Crew assist skipper. |  |  |  |
|  | Approaches head to wind/close hauled. |  |  |  |
|  | Stopped at mooring. |  |  |  |
| Crew Overboard | Keep crew in sight. |  |  |  |
|  | Stop boat to leeward of crew. |  |  |  |
| Comments |  |
| Towing | Safety Receive and Cast off line. |  |  |  |
|  | Tie towline to secure point. |  |  |  |
|  | Steer towards the motor. |  |  |  |
|  | Crew weight low and aft. |  |  |  |
|  | Centreboard half way up. |  |  |  |
|  | Skipper and Crew pay close attention to towing vessel’s commands. |  |  |  |
| Sailing by the Lee | Maintains a straight course for 90 meters. |  |  |  |
|  | Crew prevents the boom from gybing. |  |  |  |
| Out of Irons | Crew backwinds the jib. |  |  |  |
|  | Skipper steers the proper direction. |  |  |  |
| Paddle a Sailboat | Paddle a sailboat single-handed 30 meters without the use of the rudder. |  |  |  |
|  | Boat remains with 3 meters of the track. |  |  |  |
| Comments |  |
| SKILLS | - Not Demonstrated (ND) - Demonstrated (D) - Demonstrated Consistently (DC) |
| AFLOAT | ND | D | DC |  | ND | D | DC |
| Helming Skills | Beating |  |  |  | Close Reach |  |  |  |
|  | Running |  |  |  | Beam Reach |  |  |  |
|  | Tacking |  |  |  | Broad Reach |  |  |  |
|  | Gybing |  |  |  | Starboard Tack |  |  |  |
|  | Stopping |  |  |  | Port Tack |  |  |  |
|  | Hiking |  |  |  | Bearing Away |  |  |  |
|  | Luffing |  |  |  | Heading Up |  |  |  |
|  | Sail Trim |  |  |  |  |
| Comments |  |

| SKILLS | - Not Demonstrated (ND) - Demonstrated (D) - Demonstrated Consistently (DC) |
| --- | --- |
| AFLOAT | ND | D | DC |  | ND | D | DC |
| Crewing Skills | Sail Trim |  |  |  | Daggerboard |  |  |  |
|  | Lookout |  |  |  | Boat Trim |  |  |  |
|  | Gybing |  |  |  | Boomvang |  |  |  |
|  | Tacking |  |  |  |  |  |  |  |
| Comments |  |
| SKILLS | Not Demonstrated | Demonstrated | Demonstrated consistently |
| Self Recovery (from turtle position) | Check the crew. |  |  |  |
|  | Maintain a grasp of the boat. |  |  |  |
|  | Crew to bow. |  |  |  |
|  | Skipper rights boat to capsize position. |  |  |  |
|  | Skipper grasp jib sheet to right |  |  |  |
|  | Skipper to dagger/centerboard. |  |  |  |
|  | Sailboat kept head to wind. |  |  |  |
|  | Right boat under control. |  |  |  |
|  | Quick entry over transom area. |  |  |  |
|  | Bail Sailboat. |  |  |  |
|  | Recover paddles and bailer. |  |  |  |
| Comments |  |

Comments:

| Head Instructor: |  |  | Instr # |  |
| --- | --- | --- | --- | --- |
| Instructor: |  |  | Instr # |  |